## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Memory Hierarchy & Caches
Prof. Gennady Pekhimenko
University of Toronto
Fall 2019
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU and ETH

## Slide 2: Reviews: Cache Compression
Review:
  Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012

## Slide 3: Project Proposal Deadline
Deadline is on October 1st
Send emails with your proposals (PDFs) to csc2224arch@gmail.com

## Slide 4: Memory (Programmer’s View)

## Slide 5: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture
A classic example of the programmer/(micro)architect tradeoff

## Slide 6: (Physical) Memory System
You need a larger level of storage to manage a small amount of physical memory automatically
   Physical memory has a backing store: disk
We will first start with the physical memory system
For now, ignore the virtual  physical indirection
We will get back to it when the needs of virtual memory start complicating the design of physical memory…

## Slide 7: Idealism
Instruction
Supply
Pipeline
(Instruction
execution)
Data
Supply
- Zero latency access
- Infinite capacity
- Zero cost
- Perfect control flow
No pipeline stalls
Perfect data flow
(reg/memory dependencies)
Zero-cycle interconnect
(operand communication)
Enough functional units
Zero latency compute
Zero latency access
Infinite capacity
- Infinite bandwidth
Zero cost

## Slide 8: The Memory Hierarchy

## Slide 9: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 10: Ideal Memory
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)

## Slide 11: The Problem
Ideal memory’s requirements oppose each other
Bigger is slower
  Bigger  Takes longer to determine the location
Faster is more expensive
  Memory technology: SRAM vs. DRAM vs. Disk vs. Tape
Higher bandwidth is more expensive
  Need more banks, more ports, higher frequency, or faster technology

## Slide 12: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
row enable
_bitline

## Slide 13: Memory Technology: SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to persist in the “cell”
  4 transistors for storage
  2 transistors for access
row select
bitline
_bitline

## Slide 14: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 15: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row select
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row select
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. differential sensing and column select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 16: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bits stored as charges on node capacitance (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Destructive reads
Charge loss over time
Refresh: A DRAM controller must periodically read each row within the allowed refresh time (10s of ms) such that charge is restored

## Slide 17: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 18: The Problem (data from 2011)
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 10$ per Megabyte
  DRAM, < 1$ per Megabyte
  Hard Disk < 1$ per Gigabyte
  These sample values (circa ~2011) scale with time
Other technologies have their place as well
  Flash memory, PC-RAM, MRAM, RRAM (not mature yet)

## Slide 19: The Problem (Modern)
Faster is more expensive (dollars and chip area)
  SRAM, $5000 per GB
  DRAM, < $100 per GB
  SSD, < $0.50 per GB
  Hard Disk < $0.04 per GB
  NVDIMM < $10 per GB

## Slide 20: Why Memory Hierarchy?
We want both fast and large
But we cannot achieve both with a single level of memory
Idea: Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and ensure most of the data the processor needs is kept in the fast(er) level(s)

## Slide 21: The Memory Hierarchy
fast
small
big but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 22: Memory Hierarchy
Fundamental tradeoff
  Fast memory: small
  Large memory: slow
Idea: Memory hierarchy
Latency, cost, size,
bandwidth
CPU
Main
Memory
(DRAM)
RF
Cache
Hard Disk

## Slide 23: Locality
One’s recent past is a very good predictor of his/her near future.
Temporal Locality: If you just did something, it is very likely that you will do the same thing again soon
  since you are here today, there is a good chance you will be here again and again regularly
Spatial Locality: If you did something, it is very likely you will do something similar/related (in space)
  every time I find you in this room, you are probably sitting close to the same people

## Slide 24: Memory Locality
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal: A program tends to reference the same memory location many times and all within a small window of time
Spatial: A program tends to reference a cluster of memory locations at a time
  most notable examples:
    1. instruction memory references
    2. array/data structure references

## Slide 25: Caching Basics: Exploit Temporal Locality
Idea: Store recently accessed data in automatically managed fast memory (called cache)
Anticipation: the data will be accessed again soon
Temporal locality principle
  Recently accessed data will be again accessed in the near future
  This is what Maurice Wilkes had in mind:
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
    “The use is discussed of a fast core memory of, say 32000 words as a slave to a slower core memory of, say, one million words in such a way that in practical cases the effective access time is nearer that of the fast memory than that of the slow memory.”

## Slide 26: Caching Basics: Exploit Spatial Locality
Idea: Store addresses adjacent to the recently accessed one in automatically managed fast memory
  Logically divide memory into equal size blocks
  Fetch to cache the accessed block in its entirety
Anticipation: nearby data will be accessed soon
Spatial locality principle
  Nearby data in memory will be accessed in the near future
    E.g., sequential instruction access, array traversal
  This is what IBM 360/85 implemented
    16 Kbyte cache with 64 byte blocks
    Liptay, “Structural aspects of the System/360 Model 85 II: the cache,” IBM Systems Journal, 1968.

## Slide 27: The Bookshelf Analogy
Book in your hand
Desk
Bookshelf
Boxes at home
Boxes in storage
Recently-used books tend to stay on desk
  Comp Arch books, books for classes you are currently taking
  Until the desk gets full
Adjacent books in the shelf needed around the same time
  If I have organized/categorized my books well in the shelf

## Slide 28: Caching in a Pipelined Design
The cache needs to be tightly integrated into the pipeline
  Ideally, access in 1-cycle so that dependent operations do not stall
High frequency pipeline  Cannot make the cache large
  But, we want a large cache AND a pipelined design
Idea: Cache hierarchy
CPU
Main
Memory
(DRAM)
RF
Level1
Cache
Level 2
Cache

## Slide 29: A Note on Manual vs. Automatic Management
Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs
  “core” vs “drum” memory in the 50’s
  still done in some embedded processors (on-chip scratch pad SRAM in lieu of a cache) and GPUs (called “shared memory”)
Automatic: Hardware manages data movement across levels, transparently to the programmer
  ++ programmer’s life is easier
  the average programmer doesn’t need to know about it
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 30: A Modern Memory Hierarchy
Register File
32 words, sub-nsec
L1 cache
~32 KB, ~nsec
L2 cache
512 KB ~ 1MB, many nsec
L3 cache,
.....
Main memory (DRAM),
GB, ~100 nsec
Swap Disk
100 GB, ~10 msec
manual/compiler
register spilling
automatic
demand
paging
Automatic
HW cache
management
Memory
Abstraction

## Slide 31: Hierarchical Latency Analysis
For a given memory hierarchy level i it has a technology-intrinsic access time of ti, The perceived access time Ti is longer than ti
Except for the outer-most hierarchy, when looking for a given address there is
  a chance (hit-rate hi) you “hit” and access time is ti
  a chance (miss-rate mi) you “miss” and access time ti +Ti+1
  hi + mi = 1
Thus
Ti = hi·ti + mi·(ti + Ti+1)
Ti = ti + mi ·Ti+1
hi and mi are defined to be the hit-rate
and miss-rate of just the references that missed at Li-1

## Slide 32: Hierarchy Design Considerations
Recursive latency equation
Ti = ti + mi ·Ti+1
The goal: achieve desired T1 within allowed cost
Ti  ti is desirable
Keep mi low
  increasing capacity Ci lowers mi, but beware of increasing ti
  lower mi by smarter management (replacement::anticipate what you don’t need, prefetching::anticipate what you will need)
Keep Ti+1 low
  faster lower hierarchies, but beware of increasing cost
  introduce intermediate hierarchies as a compromise

## Slide 33
90nm P4, 3.6 GHz
L1 D-cache
  C1 = 16K
  t1 = 4 cyc int / 9 cycle fp
L2 D-cache
  C2 =1024 KB
  t2 = 18 cyc int / 18 cyc fp
Main memory
  t3 = ~ 50ns or 180 cyc
Notice
  best case latency is not 1
  worst case access latencies are into 500+ cycles
if m1=0.1, m2=0.1
T1=7.6, T2=36
if m1=0.01, m2=0.01
T1=4.2, T2=19.8
if m1=0.05, m2=0.01
T1=5.00, T2=19.8
if m1=0.01, m2=0.50
T1=5.08, T2=108
Intel Pentium 4 Example

## Slide 34: Cache Basics and Operation

## Slide 35: Cache
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch, e.g. a web cache
Most commonly in the on-die context: an automatically-managed memory hierarchy based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 36: Caching Basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    Maybe have to kick something else out to do it
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 37: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Aside: Can reducing AMAT reduce performance?
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 38: A Basic Hardware Cache Design
We will start with a basic hardware cache design
Then, we will examine a multitude of ideas to make it better

## Slide 39: Blocks and Addressing the Cache
Memory is logically divided into fixed-size blocks
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
Cache access:
  1) index into the tag and data stores with index bits in address
  2) check valid bit in tag store
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 40: Direct-Mapped Cache: Placement and Access
Assume byte-addressable memory: 256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location: Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data

## Slide 41: Direct-Mapped Caches
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 42: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 43: Higher Associativity
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 44: Full Associativity
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 45: Associativity (and Tradeoffs)
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time
  (hit latency and data access latency)
  -- More expensive hardware
  (more comparators)
Diminishing returns from
higher associativity
associativity
hit rate

## Slide 46: Issues in Set-Associative Caches
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)
Insertion: What happens to priorities on a cache fill?
  Where to insert the incoming block, whether or not to insert the block
Promotion: What happens to priorities on a cache hit?
  Whether and how to change block priority
Eviction/replacement: What happens to priorities on a cache miss?
  Which block to evict and how to adjust priorities

## Slide 47: Eviction/Replacement Policy
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used (how to implement?)
    Not most recently used
    Least frequently used?
    Least costly to re-fetch?
      Why would memory accesses have different cost?
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 48: Implementing LRU
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way set associative cache:
  What do you need to implement LRU perfectly?
  How many different orderings possible for the 4 blocks in the set?
  How many bits needed to encode the LRU order of a block?
  What is the logic needed to determine the LRU victim?

## Slide 49: Approximations of LRU
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)
Examples:
  Not MRU (not most recently used)
  Hierarchical LRU: divide the N-way set into M “groups”, track the MRU group and the MRU way in each group
  Victim-NextVictim Replacement: Only keep track of the victim and the next victim

## Slide 50: Hierarchical LRU (not MRU)
Divide a set into multiple groups
Keep track of only the MRU group
Keep track of only the MRU block in each group
On replacement, select victim as:
  A not-MRU block in one of the not-MRU groups (randomly pick one of such blocks/groups)

## Slide 51: Cache Replacement Policy: LRU or Random
LRU vs. Random: Which one is better?
  Example: 4-way cache, cyclic references to A, B, C, D, E
    0% hit rate with LRU policy
Set thrashing: When the “program working set” in a set is larger than set associativity
  Random replacement policy is better when thrashing occurs
In practice:
  Depends on workload
  Average hit rate of LRU and Random are similar
Best of both Worlds: Hybrid of LRU and Random
  How to choose between the two? Set sampling
    See Qureshi et al., “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 52: What Is the Optimal?
Belady’s OPT
  Replace the block that is going to be referenced furthest in the future by the program
  Belady, “A study of replacement algorithms for a virtual-storage computer,” IBM Systems Journal, 1966.
  How do we implement this? Simulate?
Is this optimal for minimizing miss rate?
Is this optimal for minimizing execution time?
  No. Cache miss latency/cost varies from block to block!
  Two reasons: Remote vs. local caches and miss overlapping
  Qureshi et al. “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 53: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 54: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 55: Handling Writes (II)
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can combine writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires (?) transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 56: Handling Writes (III)
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Ditto for a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes

## Slide 57: Cache Performance

## Slide 58: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 59: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 60: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each with V bit)
      Can improve “write” performance
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and
  bandwidth/energy:
  if spatial locality is not high
hit rate
block
size

## Slide 61: Paper Review #1: Summary
Contents and merits are summarized well
Main problems are in weaknesses and future work parts
Unjustified claims or too high-level
  "I don't believe ... is a realistic assumption“
  "the paper should provide possible future research direction"
  We can list more specific examples on what can be done differently/better
Notes: Therefore, the authors' conclusion will not be affected unless people can show that some components (e.g. hardware accelerators that most people talk about) can greatly boost the system performance without introducing must power or area overhead.

## Slide 62: Paper Review #1: Grades Distribution
Chart: Grade Distribution
| 8 | 9 | 10
Grades (out of 10) | 2 | 5 | 3

## Slide 63: Review #3: Cache Compression
Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012

## Slide 64: CSC 2224: Parallel Computer Architecture and Programming Memory Hierarchy & Caches
Prof. Gennady Pekhimenko
University of Toronto
Fall 2019
The content of this lecture is adapted from the lectures of
Onur Mutlu @ CMU and ETH