## Slide 1: CSC 2224: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 2: Review #4
RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization Vivek Seshadri et al., MICRO 2013

## Slide 3: Why Is Memory So Important? (Especially Today)

## Slide 4: The Performance Perspective
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 5: The Energy Perspective
Dally, HiPEAC 2015

## Slide 6: The Energy Perspective
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 7: The Reliability Perspective
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 8: The Security Perspective
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 9: Why Is DRAM So Slow?

## Slide 10: Motivation (by Vivek Seshadri)
Conversation with a friend from Stanford
Why is DRAM so slow?!
Really?
50 nanoseconds to serve one request? Is that a fundamental limit to DRAM’s access latency?
Him
Vivek

## Slide 11: Understanding DRAM
What is in here?
DRAM
Problems related to today’s DRAM design
Solutions proposed by our research

## Slide 12: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013, Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 13: What is DRAM?
DRAM – Dynamic Random Access Memory
3455434
Array of Values
43543
98734
0
847
42
873909
1729
WRITE address, value
READ address
Accessing any location takes the same amount of time
Data needs to be constantly refreshed
Notes: DRAM stands for Dynamic Random Access Memory.
Memory, as many of may know, is a device that can store information and allow the information to be retrieved at a later point in time. The simplest abstraction for memory is an array of fixed-size values. We can read from a location by specifying its address or write to a location by providing its address and the value to be written.
A random access memory is one in which accessing any location takes the same amount of time.
The dynamic part of DRAM refers to the fact that DRAM loses data when left alone.

## Slide 14: DRAM in Today’s Systems
Why DRAM? Why not some other memory?
Notes: DRAM memory is an integral part of most computing systems today. Desktops, laptops, mobile phones, large servers; all of them have DRAM based memory.
In fact, if you ever wondered why your laptops have a separate sleep mode and hibernate mode, the dynamic part of DRAM is one of the primary reasons. In the sleep mode, the DRAM in your laptop is still powered on and kept in a state where it does not lose its data. In the hibernate mode, the data in DRAM is written to the hard disk and the system is completely shutdown.
Why DRAM? Why not some other memory?

## Slide 15: Von Neumann Model
Processor
Memory
Program
Data
T1 = Read Data[1]
T2 = Read Data[2]
T3 = T1 + T2
Write Data[3], T3
3
4
8
2
T1 = Read Data[1]
4
4 instruction accesses +
3 data accesses
Memory performance is important

## Slide 16: Factors that Affect Choice of Memory
Speed
  Should be reasonably fast compared to processor
Capacity
  Should be large enough to fit programs and data
Cost
  Should be cheap
Notes: There are three factors that affect the choice of memory in a system.
Speed, Capacity and Cost. Blah..
In fact, as we will see in this talk, cost is one of the primary factors that drives decisions taken by the industry.

## Slide 17: Why DRAM?
Access Latency
Cost
Flip-flops
SRAM
DRAM
Flash
Disk
Higher Cost
Higher access latency
Favorable point in the trade-off spectrum
Notes: In contrast, DRAM is at a favorable point in this trade-off spectrum between cost and latency. And it is going to remain so for the foreseeable future.

## Slide 18: Is DRAM Fast Enough?
Processor
Commodity DRAM
Request
3 GHz, 2 Instructions / cycle
300 Instructions
300 Instructions
300 Instructions
300 Instructions
Independent programs
Request
Request
Request
Served in parallel?
Core
Core
Core
Core
Latency
Parallelism
50ns
Notes: Is DRAM fast enough? Let us try to understand this using today’s processor and DRAM technology. The DRAM we can buy today, which I will refer to as commodity DRAM, takes 50ns to serve a request. A modern processor running at 3Ghz and executing 2 instructions every cycle can run up to 300 instructions in the same duration. To make matters worse, modern processors have multiple cores which can independently execute different programs. If each of these programs independently generate memory requests, the question is whether DRAM can serve the requests in parallel? If the independent requests are served serially, then the cores will have to wait for much longer before doing any useful work. So, there are two problems related to DRAM that we need to address: Latency and Parallelism.

## Slide 19: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013, Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 20
processor
main memory
peripheral logic
bank
mat
high latency
DRAM Organization
Notes: Right figure shows the picture of real DRAM chip,
which consists of multiple banks and peripheral logic for accessing cells in banks.
Each bank is subdivided into multiple mats.

## Slide 21
DRAM Cell Array: Mat
peripheral logic
cell
mat
mat
sense amplifier
wordline driver
cell
wordline
bitline
Notes: A mat consists of 2d cell array.
The cells are horizontally connected to wordline driver by wordline,
and vertically connected to a sense amplifier by bitline.

## Slide 22: Memory Element (Cell)
0
1
Component that can be in at least two states
Can be electrical, magnetic, mechanical, etc.
DRAM → Capacitor

## Slide 23: Capacitor – Bucket of Electric Charge
Charge
“Charged”
“Discharged”
0
0
Vmax
0
Voltage level indicator. Not part of the actual circuit

## Slide 24: DRAM Chip
Contains billions of capacitors (also called cells)
0
?
DRAM Chip

## Slide 25: Divide and Conquer
DRAM Bank
?
Weak
Reading destroys state
Challenges

## Slide 26: Sense-Amplifier
Vmax
0
Vx
Vy
Vx > Vy
Vx
Vy
Vx+δ
Vx+δ
Vy-δ
Amplify the difference
Stable state

## Slide 27: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 28: DRAM Cell Read Operation
Vmax/2
Vmax/2
0
Vmax/2 + δ
0
Vmax
Vmax
Vmax/2 + δ
DRAM
Cell
Sense-Amplifier
Cell loses charge
Amplify the difference
Restore Cell Data
Access data
1
2

## Slide 29: DRAM Cell Read Operation
0
DRAM
Cell
Sense-Amplifier
Control Signal
DRAM
Cell
Address

## Slide 30: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 31: Problem
Sense-Amplifier
Control Signal
DRAM
Cell
Address
Much larger than a cell

## Slide 32: Cost Amortization
Bitline
Wordline

## Slide 33: DRAM Array Operation
1
0
0
1
1
0
1
0
0
1
0
1
½
½
½
½
½
½
½
½
½
½
½
½
Row Decoder
1
Row Address
?
?
?
?
?
?
?
?
?
?
?
?
↑½
↑½
↑½
↑½
↑½
↑½
½↓
½↓
½↓
½↓
½↓
½↓
m
1
0
0
1
1
0
1
0
0
1
0
1
Sensing & Amplification
Charge Restoration
Wordline Disable
Charge Sharing
Wordline Enable
Access Data (column n)
Restore
Sense-Amplifier
m
n
Sense-Amplifiers

## Slide 34: Outline
What is DRAM?
DRAM Internal Organization
  DRAM Cell
  DRAM Array
  DRAM Bank
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013 Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 35: DRAM Bank
How to build a DRAM bank from a DRAM array?

## Slide 36: DRAM Bank: Single DRAM Array?
10000+ rows
Row Decoder
1
0
0
1
1
0
0
1
Long bitline
Difficult to sense data in far away cells
Row Address

## Slide 37: DRAM Bank: Collection of Arrays
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Data
Subarray

## Slide 38: DRAM Operation: Summary
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row m, Col n
m
1. Enable row m
2. Access col n
3. Close row
n
m

## Slide 39: DRAM Chip Hierarchy
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Collection of Banks
Collection of Subarrays

## Slide 40: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 41: Factors That Affect Performance
Latency
  How fast can DRAM serve a request?
Parallelism
  How many requests can DRAM serve in parallel?

## Slide 42: DRAM Chip Hierarchy
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Collection of Banks
Collection of Subarrays
Latency
Parallelism

## Slide 43: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013; Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 44: Subarray Size: Rows/Subarray
Number of rows in subarray
Latency
Chip Area

## Slide 45: Subarray Size vs. Access Latency
Smaller subarrays => lower access latency
Shorter Bitlines => Faster access

## Slide 46: Subarray Size vs. Chip Area
Large Subarray
Smaller Subarrays
Area
Cost
Smaller subarrays => larger chip area

## Slide 47: Chip Area vs. Access Latency
Chart: Access Latency (ns)
| 23.10725021132788 | 24.617764350044737 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
Commodity DRAM
(512 rows/subarray)
32 rows/subarray
Why is DRAM so slow?

## Slide 48: Chip Area vs. Access Latency
Chart: Access Latency (ns)
| 23.10725021132788 | 24.617764350044741 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
Commodity DRAM
(512 rows/subarray)
32 rows/subarray
?
How to enable low latency without high area overhead?

## Slide 49: New Proposal
Large Subarray
Small Subarray
Our Proposal
Low area cost

## Slide 50: Tiered-Latency DRAM
Near Segment
Far Segment
+ Lower access latency
+ Lower energy/access
- Higher access latency
- Higher energy/access
Map frequently accessed data to near segment

## Slide 51: Results Summary
Chart: 
| Performance
Commodity DRAM | 1
TL-DRAM | 1.12
Chart: 
| Energy Consumption
Commodity DRAM | 1
TL-DRAM | 0.73
12%
23%
Commodity DRAM
Tiered-Latency DRAM

## Slide 52: Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, Onur Mutlu
Published in the proceedings of 19th IEEE International Symposium on
High Performance Computer Architecture 2013

## Slide 53
DRAM Stores Data as Charge
1. Sensing
2. Restore
3. Precharge
DRAM cell
Sense amplifier
Three steps of charge movement
Notes: The right figure shows DRAM organization which is consists of DRAM cells and sense-amplifiers.
There are three steps for accessing DRAM.
First, when DRAM selects one of rows in its cell array, the selected cells drive their charge to sense-amplifiers.
Then, sense-amplifiers detect the charge, recognizing data of cells.
We call this operation as sensing.
Second, after sensing data from DRAM cells, sense-amplifiers drive charge to the cells for reconstructing original data.
We call this operation as restore.
Third, after restoring the cell data, DRAM deselects the accessed row and puts the sense-amplifiers to original state for next access.
We call this operation as precharge.
As shown in these three steps, DRAM operation is charge movement between cell and sense-amplifier.

## Slide 54
Sensing
Restore
Timing Parameters
Data 0
Data 1
cell
time
charge
Sense amplifier
DRAM Charge over Time
Why does DRAM need the extra timing margin?
In theory
margin
cell
Sense amplifier
In practice
Notes: Timing parameters exist to ensure sufficient movement of charge.
The figure shows the timeline for accessing DRAM in X-axis and Y-axis shows the charge amount in DRAM cell and sense-amplifier.
When selecting a row of cells, each cell drives their charge toward to the corresponding sense-amplifier.
If driven charge is more than enough to detect the data, the sense-amplifier starts to restore data by driving charge toward the cell.
This restore operation finishes when the cell is fully charged.
Ideally, DRAM timing parameters are just enough for the sufficient movement of charge.
However, in practice, there are large margin in DRAM timing parameters.
Why are these margin required?

## Slide 55
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge;
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 56
Same size 
Same charge 
Different size 
Different charge 
Same latency
Different latency
Large variation in cell size 
Large variation in charge 
Large variation in access latency
DRAM Cells are Not Equal
Real
Ideal
Largest cell
Smallest cell
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 57
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 58
Cells store small charge at high temperature
and large charge at low temperature
 Large variation in access latency
Charge Leakage Temperature
Room Temp.
Hot Temp. (85°C)
Small leakage
Large leakage
Notes: DRAM leakage increases the variation.
DRAM loses their charge over time and loses more charge at higher temperature.
Therefore, DRAM cell has smallest charge when operating at hot temperature, for example 85C which is the highest temperature guaranteed by DRAM standard.
This temperature dependence increases the variation in DRAM cell charge.

## Slide 59
DRAM Timing Parameters
DRAM timing parameters are dictated by the worst case
  The smallest cell with the smallest charge in all DRAM products
  Operating at the highest temperature
Large timing margin for the common case
Can lower latency for the common case

## Slide 60: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is the photo of our infrastructure, that we built mostly from scratch.
For higher throughput, we employ eight FPGAs, all of which are enclosed in thermally-regulated environment.

## Slide 61
Typical DIMM at
Low Temperature
Obs 1. Faster Sensing
More charge
Strong charge
flow
Faster sensing
Typical DIMM at Low Temperature
 More charge  Faster sensing
Timing
(tRCD)
17% ↓
No Errors
115 DIMM
characterization
Notes: First step in DRAM operation is sensing.
In typical case, there are more charge in DRAM cell compared to the worst case.
The excessive charge enables stronger charge drive to sense-amplifier.
Then, sense-amplifier can detect data of DRAM cell fast, thereby complete sensing operation fast.
In our DRAM latency profiling results of 115 DRAM modules,
we observe that 17% potential reduction for the corresponding timing parameters of sensing.
As a result, more charge in typical cases lead to fast sensing.

## Slide 62
Obs 2. Reducing Restore Time
Larger cell &
Less leakage 
Extra charge
No need to fully
restore charge
Typical DIMM at lower temperature
 More charge  Restore time reduction
Read (tRAS)
37% ↓
Write (tWR)
54% ↓
No Errors
115 DIMM
characterization
Typical DIMM at
Low Temperature
Notes: Second step in DRAM operation is restore.
Due to larger size and less leakage, typical DRAM cells have more charge than the worst cell.
Even though typical DRAM does not restore the excessive charge during restore operation,
eventually the typical cell has more charge than the worst case cell, guaranteeing reliable operations.
By reducing this restore time in DRAM read/write, our DRAM latency characterization shows significant potential to reduce corresponding timing parameters. For example, 37% for read and 54% for write.
As a result, more charge in typical cases enables restore time reduction.

## Slide 63
Empty (0V)
Full (Vdd)
Half
Obs 3. Reducing Precharge Time
Bitline
Sense amplifier
Sensing
Precharge
Precharge ?
– Setting bitline to half-full charge
Typical DIMM at
Low Temperature
Notes: Third step is precharge. Previously we explained the precharge simply as going back to original state.
Let me introduce more details about precharge.
To detect data in DRAM cell, DRAM has sense-amplifier and wire connection to the bitline.
DRAM preserve their a bit of data in two charge state, empty and fully charged.
During sensing and restore, the bitline moves to either of these two states.
After finishing the access, the bitline should be go back to the half of these two state.
We call this precharge. Unfortunately, bitline is usually long by connecting hundred of cells such that it takes long time for precharge.

## Slide 64
Empty (0V)
Full (Vdd)
Half
bitline
Not fully precharged
More charge
 strong sensing
Access empty cell
Access full cell
Timing
(tRP)
35% ↓
No Errors
115 DIMM
characterization
Typical DIMM at Lower Temperature
 More charge  Precharge time reduction
Obs 3. Reducing Precharge Time
Notes: Let us observe the impact of reducing precharge with a simple example.
The sense-amplifier first accesses an empty cell then not fully precharged by reducing corresponding timing parameter.
Then DRAM next access a fully charged cell.
Due to the bias in the bitline, it takes longer time to access the fully charged cell.
However, if the cell has much excessive charge, the strong charge flow overcomes the bias in the bitline, leading to reliable access.
Our DRAM latency evaluation shows that in typical case, we can reduce corresponding timing parameter by 35% without errors.
Therefore, more charge in typical cases enables precharge time reduction.

## Slide 65: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer profiles multiple sets of
  reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature

## Slide 66
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi-Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
Real System Evaluation
AL-DRAM provides high performance improvement, greater for multi-core workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 67
Summary: AL-DRAM
Observation
  DRAM timing parameters are dictated by the worst-case cell (smallest cell at highest temperature)
Our Approach: Adaptive-Latency DRAM (AL-DRAM)
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)
Notes: Let me summarize.
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 68: Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case
Donghyuk Lee, Yoongu Kim,
Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu
Published in the proceedings of 21st
International Symposium on High Performance Computer Architecture 2015

## Slide 69: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013;
  Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 70: Parallelism: Demand vs. Supply
Demand
Supply
Out-of-order Execution
Multi-cores
Prefetchers
Multiple
Banks

## Slide 71: Increasing Number of Banks?
How to improve available parallelism within DRAM?
Adding more banks → Replication of shared structures
Replication → Cost

## Slide 72: Our Observation
Time
1. Wordline enable
2. Charge sharing
3. Sense amplify
4. Charge restoration
5. Wordline disable
6. Restore sense-amps
Data Access
Local to a subarray

## Slide 73: Subarray-Level Parallelism
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row Address
Row Address
Replicate
Time share

## Slide 74: Subarray-Level Parallelism: Benefits
Time
Data Access
Data Access
Data Access
Data Access
Saved Time
Commodity DRAM
Subarray-Level Parallelism
Two requests to different subarrays in same bank

## Slide 75: Results Summary
Chart: 
| Performance
Commodity DRAM | 1
SALP | 1.17
Chart: 
| Energy Consumption
Commodity DRAM | 1
SALP | 0.81
Commodity DRAM
Subarray-Level Parallelism
17%
19%

## Slide 76: A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, Onur Mutlu
Published in the proceedings of 39th
International Symposium on Computer Architecture 2012

## Slide 77: Review #4
RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization Vivek Seshadri et al., MICRO 2013

## Slide 78: CSC 2224: Parallel Computer Architecture and Programming Main Memory Fundamentals
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU